## Slide 1: Computer Networks CS358
Instructor: Joydeep Chandra

## Slide 2: Course Outline
Theory
  Basics of Interworking
  Modern Networking Applications and Technologies
  Advanced Concepts in Design of Network based Applications
Lab
  Implementation of networking protocols
  Use of simulators
  Develop network based applications

## Slide 3: Evaluation
Theory + Lab
  Either 60-40 or 70-30 (TBD)
Theory
  Quizzes and Class Tests 20%
  MidSem 30%
  End Sem 50%
Lab
  Assignments 50%
  MidSem 20%
  EndSem 30%

## Slide 4: Books and References
Text Book
  James F. Kurose and Keith W. Ross, Computer Networking: A Top-Down Approach
  Forouzan, Data Communications and Networking
References
  Larry L. Peterson and Bruce S. Davie, Computer Networks, A Systems Approach
  Tenenbaum and Wetherall, Computer Networks, Pearson India, 5th Edition
  Some research articles and papers

## Slide 5
Chapter 1 Introduction
Computer Networking: A Top Down Approach , 4th edition. Jim Kurose, Keith Ross Addison-Wesley, July 2007.
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) in substantially unaltered form, that you mention their source (after all, we’d like people to use our book!)
If you post any slides in substantially unaltered form on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2007
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 6: Outline
  Internet architecture
  Internet history
  Today’s Internet
  Internet in a nutshell (protocols in practice)

## Slide 7: Internet Architecture
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt

## Slide 8: Why did the Internet win?
Packet switching over circuit switching
End-to-end principle and “Hourglass” design
Layering of functionality
Distributed design, decentralized control
Superior organizational process

## Slide 9: Circuit Switching
Circuit switching:
  There is a dedicated communication path between two stations (end-to-end)
  The path is a connected sequence of links between network nodes. On each physical link, a logical channel is dedicated to the connection.
Communication via circuit switching has three phases:
  Circuit establishment (link by link)
    Routing & resource allocation (FDM or TDM)
  Data transfer
  Circuit disconnect
    Deallocate the dedicated resources
The switches must know how to find the route to the destination and how to allocate bandwidth (channel) to establish a connection.

## Slide 10: Circuit Switching Properties
Inefficiency
  Channel capacity is dedicated for the whole duration of a connection
  If no data, capacity is wasted
Delay
  Long initial delay: circuit establishment takes time
  Low data delay: after the circuit establishment, information is transmitted at a fixed data rate with no delay other than the propagation delay. The delay at each node is negligible.
Developed for voice traffic (public telephone network) but can also applied to data traffic.
  For voice connections, the resulting circuit will enjoy a high percentage of utilization because most of the time one party or the other is talking.
  But how about data connections?

## Slide 11: Public Circuit Switched Network
Subscribers: the devices that attach to the network.
Subscriber loop: the link between the subscriber and the network.
Exchanges: the switching centers in the network.
End office: the switching center that directly supports subscribers.
Trunks: the branches between exchanges. They carry multiple voice-frequency circuits using either FDM or synchronous TDM.

## Slide 12: Packet vs. circuit switching
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 13: Circuit Switching
End-end resources reserved for “call”
network resources (e.g., bandwidth) divided into “pieces”
  link bandwidth, switch capacity
  pieces allocated to calls
  resource piece idle if not used by owning call
    dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup and admission control required

## Slide 14: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 15: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!

## Slide 16: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
  1,536,000/24 = 64000 bps per time slot
  640000bits/64000bps = 10 sec.
  Total time = 500 msec + 10 sec = 10.5 sec

## Slide 17: Case study: Circuit Switching
1890-current: Phone network
  Fixed bit rate
  Mostly voice
  Not fault-tolerant
  Components extremely reliable
  Global application-level knowledge throughout network
  Admission control at local switching station (dial-tone)

## Slide 18: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 19: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, shared on demand  statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 20: Packet switching versus circuit switching
N users over 1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
  Allows more users to use network
  “Statistical multiplexing gain”
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 21: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Bad for applications with hard resource requirements
  Excessive congestion: packet delay and loss
  Need protocols for reliable data transfer, congestion control
  Applications must be written to handle congestion
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
  Common practice: over-provision
Is packet switching a “slam dunk winner?”

## Slide 22: Problems with packet switching
Packet loss and queuing delay
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
when packet arrives to full queue, packet is dropped (aka lost)
  lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 23: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 24: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing

## Slide 25: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 26: Transmission delay example
Packet switching
  Store-and-forward
  Packet completely received before being transmitted to next node
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 27: Problem
Consider a packet of length L that begins at system A, travels over one link to a packet switch over a second link to a destination end system.
Let di, si and Ri denote the length, propagation speed and transmission rate of link i, for i=1,2.
The packet switch delays each packet by dproc
Assuming no queuing delays, what is the total end-to-end delay?
R1
R2
L

## Slide 28: Problem
A router buffer of infinite size has certain queuing delay. Let L be the size of packets coming to the router and R be the rate(bits/sec) at which packets are sent out of the queue. What is the average routing delay if N packets arrive simultaneously every NL/R seconds.

## Slide 29: Case study: Packet Switching
1970/80s-current: Internet network
  Variable bit rate
  Mostly data
  Fault-tolerant
  Components not extremely reliable (versus phone components)
  Distributed control and management

## Slide 30: Why did the Internet win?
Packet switching over circuit switching
End-to-end principle and “Hourglass” design
Layering of functionality
Distributed design, decentralized control
Superior organizational process

## Slide 31: End-to-end principle and Hourglass design

## Slide 32: End-to-end principle
J. H. Saltzer, D. P. Reed and D. D. Clark “End-to-end arguments in system design”, Transactions on Computer Systems, Vol. 2, No. 4, 1984
http://www.acm.org/pubs/citations/journals/tocs/1984-2-4/p277-saltzer/

## Slide 33: Hourglass design
D. Clark, “The design philosophy of the DARPA Internet”, SIGCOMM 1988, August 16 - 18, 1988.
http://www.acm.org/pubs/citations/proceedings/comm/52324/p106-clark/

## Slide 34: End-to-end principle
Where to put the functionality?
  In the network? At the edges?
End-to-end functions best handled by end-to-end protocols
  Network provides basic service: data transport
  Intelligence and applications located in or close to devices at the edge
  Violate principle as a performance enhancement
Leads to innovation at the edges
  Phone network: dumb edge devices, intelligent network
  Internet: dumb network, intelligent edge devices

## Slide 35: Hourglass design
End-to-end principle leads to “Hourglass” design of protocols
Only one protocol at the Internet level
  Minimal required elements at narrowest point
IP – Internet Protocol
  http://www.rfc-editor.org/rfc/rfc791.txt
  http://www.rfc-editor.org/rfc/rfc1812.txt
  Unreliable datagram service
  Addressing and connectionless connectivity
  Fragmentation and assembly

## Slide 36: Hourglass design
Simplicity allowed fast deployment of multi-vendor, multi-provider public network
  Ease of implementation
  Limited hardware requirements (important in 1970s)
    Is it relevant now with today’s semiconductor speeds?
  Eventual economies of scale
Designed independently of hardware
  No link-layer specific functions
  Hardware addresses decoupled from IP addresses
  IP header contains no data/physical link specific information
  Allows IP to run over any fabric

## Slide 37: Hourglass design
Waist expands at transport layer
Two dominant services layered above IP
TCP – Transmission Control Protocol
  Connection-oriented service
  http://www.rfc-editor.org/rfc/rfc793.txt
UDP – User Datagram Protocol
  Connectionless service
  http://www.rfc-editor.org/rfc/rfc768.txt

## Slide 38: Hourglass design
TCP – Transmission Control Protocol
  Reliable, in-order byte-stream data transfer
    Acknowledgements and retransmissions
  Flow control
    Sender won’t overwhelm receiver
  Congestion control
    Senders won’t overwhelm network
UDP – User Datagram Protocol
  Unreliable data transfer
  No flow control
  No congestion control

## Slide 39: Hourglass design
What uses TCP?
  HTTP, FTP, Telnet, SMTP, NNTP, BGP, IMAP, POP
What uses (mainly) UDP?
  SNMP, NTP, NFS, RTP (streaming media, IP telephony, teleconferencing), multicast applications
  Many protocols can use both
Check out /etc/services on *nix or C:\WIN*\system32\services
IANA
  http://www.iana.org/assignments/port-numbers

## Slide 40: Hourglass design
Question?
  Are TCP, UDP, and IP enough?
  What other functionality would applications need?

## Slide 41: Hourglass design
Security?
  IPsec/SSL/TLS
Quality-of-service?
  RSVP, int-serv, diff-serv
Reliable, out-of-order delivery service?
  SCTP
Handling greedy sources?
Accounting and pricing support?

## Slide 42: End-to-end principle and the Hourglass design
The good
  Basic network functionality allowed for extremely quick adoption and deployment using simple devices
The bad
  New network features and functionality are impossible to deploy, requiring widespread adoption within the network
  IP Multicast, QoS

## Slide 43: Why did the Internet win?
Packet switching over circuit switching
End-to-end principle and “Hourglass” design
Layering of functionality
Distributed design, decentralized control
Superior organizational process

## Slide 44: Layering
Modular approach to network functionality
  Simplifies complex systems
    Each layer relies on services from layer below and exports services to layer above
  Hides implementation
  Eases maintenance and updating of system
    Layer implementations can change without disturbing other layers (black box)

## Slide 45: Layering
Examples:
  Topology and physical configuration hidden by network-layer routing
    Applications require no knowledge of routes
    New applications deployed without coordination with network operators or operating system vendors
Link hardware
Host-to-host connectivity
Application

## Slide 46: Layering essential in Protocols
Set of rules governing communication between network elements (applications, hosts, routers)
Protocols specify:
  Interface to higher layers (API)
  Interface to peer
    Format and order of messages
    Actions taken on receipt of a message
  Interface defines interaction
Notes: Human analogy – social customs

## Slide 47: Layering: OSI Model
Physical
  how to transmit bits
Data link
  how to transmit frames
Network
  how to route packets host-to-host
Transport
  how to send packets end2end
Session
  how to tie flows together
Presentation
  byte ordering, formatting
Application: everything else
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical

## Slide 48: Layering: Internet protocols
application: (L7 & L6 of OSI) supporting network applications
  FTP, SMTP, HTTP
transport: (L5 & L4 of OSI) host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 49: Layers in action
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch

## Slide 50: Layering
Is Layering always good?
  Sometimes not..
    Layer N may duplicate lower level functionality (e.g., error recovery)
    Layers may need same info (timestamp, MTU)
    Strict adherence to layering may hurt performance

## Slide 51: Why did the Internet win?
Packet switching over circuit switching
End-to-end principle and “Hourglass” design
Layering of functionality
Distributed design, decentralized control
Superior organizational process

## Slide 52: Distributed design and control
Requirements from DARPA
  Must survive a nuclear attack
Reliability
  Intelligent aggregation of unreliable components
  Alternate paths, adaptivity
Distributed management & control of networks
  Allows individual networks to independently develop without large amounts of coordination
  Exceptions: TLDs and TLD servers, IP address allocation (ICANN)

## Slide 53: Superior organizational process
IAB/IETF process allowed for quick specification, implementation, and deployment of new standards
  Free and easy download of standards
  Rough consensus and running code
  2 interoperable implementations
  Bake-offs
  http://www.ietf.org/
ISO/OSI
  Comparison to IETF left as an exercise

## Slide 54: Problem 1
Consider the queuing delay in a router buffer (preceding an outbound link). Suppose all packets are L bits, the transmission rate is R bps and that N packets simultaneously arrive at the buffer every LN/R seconds. Find the average queuing delay of a packet

## Slide 55: Internet history

## Slide 56: How old is the Internet?
Guesses?
Hint
  It used to be the case that everyone in this class remembered the “pre-Internet” days

## Slide 57: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in early military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demonstration
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 58: Internet History
1970’s: proprietary network architectures developed: DECnet, SNA, XNA
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 59: Internet History
1983: deployment of TCP/IP
1983: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
Late 1980s, Early 1990s: new national networks: Csnet, BITnet, NSFnet, Minitel
  100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 60: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
late 1990’s: commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps

## Slide 61: Internet History
2007:
~500 million hosts
Voice, Video over IP
P2P applications: BitTorrent (file sharing) Skype (VoIP), PPLive (video)
more applications: YouTube, gaming
wireless, mobility

## Slide 62: Internet in a nutshell (protocols in practice)

## Slide 63: A day in the life of an Internet host…
Booting
  Dynamically configure network settings
    DHCP request
      UDP (unreliable datagrams)
      IP and data-link broadcast
    DHCP response from listening server
      IP address of host
      Netmask (i.e. 255.255.255.0) to determine network ID
      Default router
      Local DNS server

## Slide 64: A day in the life of an Internet host…
Web request http://www.yahoo.com/index.html
  Step #1: Locate DNS server
    if (netmask & IPHost == netmask & IPDNS) {
      DNS server on local network
      ARP for hardware address of IPDNS
    } else {
      DNS server on remote network
      ARP for hardware address of IPDefaultRouter
    }
    ARP (Address Resolution Protocol)
      IP address to hardware address mapping
      Request broadcast for all hosts on network to see
      Reply broadcast for all hosts to cache

## Slide 65: A day in the life of an Internet host…
Step #2: ARP request and reply

## Slide 66: A day in the life of an Internet host…
Step #3: DNS request/reply
  UDP, IP, data-link header
  DNS request to local DNS server from host
  DNS reply from local DNS server to host

## Slide 67: A day in the life of an Internet host…
Step #4: TCP connection establishment
  TCP 3-way handshake (SYN, SYN-ACK, ACK)
  Session establishment to support reliable byte stream

## Slide 68: A day in the life of an Internet host…
Step #5: HTTP request and reply
    HTTP (application data), TCP, IP, data-link header
    HTTP request
    HTTP reply

## Slide 69: tcpdump example
http://thefengs.com/wuchang/work/courses/cs594/trace.txt
ren.cse.ogi.edu
129.95.50.113
129.95.50.0/24
church.cse.ogi.edu
129.95.50.2
cse2-gw.net.ogi.edu
129.95.50.54
www.cse.ogi.edu
129.95.20.2

## Slide 70: A day in the life of an Internet host…
Role of TCP and UDP?
Demultiplex at end hosts.
  Which process gets this request?
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
TCP/UDP
IP
IPX
Port Number
Network
Protocol Field
Type Field

## Slide 71: A day in the life of an Internet host….
What about….
  Reliability
    Corruption
    Lost packets
  Flow and congestion control
  Fragmentation
  Out-of-order delivery
The beauty of TCP, IP, and layering
  All taken care of transparently

## Slide 72: What if the Data is Corrupted?
Internet
GET windex.html
GET index.html
Solution: Add a checksum
Problem: Data Corruption
0,9
9
6,7,8
21
4,5
7
1,2,3
6
X

## Slide 73: What if the Data is Lost?
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 74: What if receiver has no resources (flow control)?
Internet
PUT remix.mp3
Problem: Overflowing receiver buffers
Internet
Solution: Receiver advertised window
PUT remix.mp3
16KB free

## Slide 75: What if Network is Overloaded?
Short bursts: buffer
What if buffer overflows?
  Packets dropped and retransmitted
  Sender adjusts rate until load = resources
Called “Congestion control”

## Slide 76: What if the Data Doesn’t Fit?
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 77: What if the Data is Out of Order?
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.th
inde
ml
GET x.thindeml
GET index.html
ml
4
inde
2
x.th
3
GET
1

## Slide 78: The rest of the course
From birds-eye view, we will now focus on specific components
Review these lectures for perspective when looking at the components
Mostly classical material with some references to newer technologies

## Slide 79: Acknowledgements
Material taken from course slides by Srini Seshan’s Computer Networking course at http://www.cs.cmu.edu/~srini/15-744/S01/

## Slide 80: Extra slides

## Slide 81: Layering
Need for exposing underlying layers for optimal application performance
  D. Tennenhouse and D. Clark. Architectural Considerations for a New Generation of Protocols. SIGCOMM 1990.
  Application Layer Framing (ALF)
    Enable application to process data as soon as it can
    Expose application processing unit (ADU) to protocols
  Integrated Layer Processing (ILP)
    Layering convenient for architecture but not for implementations
    Combine data manipulation operations across layers

## Slide 82: Residential access: cable modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 83: Cable Network Architecture: Overview

## Slide 84: Residential access: cable modems

## Slide 85: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 27Mbps downstream, 2 Mbps upstream
  Limited upstream bandwidth due to multiple noise sources vs. downstream case with one controllable noise source (headend)
network of cable and fiber attaches homes to ISP router
  homes share access to router
deployment: available via cable TV companies

## Slide 86: UMass Campus Network

## Slide 87: Internet History
Those who ignore the past are doomed to repeat it
  http://www.worldcom.com/about_the_company/cerfs_up/
Where did it come from?
Who built it?
Why does it work?
Most of the original designers (old-timers) still around and active…
  internet-history-request@postel.org

## Slide 88: Internet timeline
1961 Kleinrock proposes packet switching
1962 Licklider proposes “galactic” network
  Goes to DARPA as head of CS research
1966 Roberts proposes galactic network using packet switching
  Goes to ARPA to build it (ARPANET)
1968 RFQs to build routers (Interface Message Processors)
1968 Kahn separates hardware addresses from network addresses
  ARPANET to run over any hardware
1969 Crocker initiates RFC notes to document protocols
  Freely available
1969 First node of ARPANET UCLA (September)
1969 4-node ARPANET at UCLA, SRI, Utah, UCSB (December)
  Initial hosts.txt name database
1970 Crocker develops NCP (host-to-host protocol for applications)
  Precursor to TCP
1972 Tomlinson develops e-mail (@)

## Slide 89: Internet timeline
1972 Issues with NCP and ARPANET arise
  NCP relied on ARPANET for end2end reliability (assumed no packet loss)
    Can not work over satellite or packet radio links
  NCP addressing tied to ARPANET
1973 Kahn redesigns protocols
  Communication on a “best-effort” basis
    Least-common denominator
    End points in charge of retransmission, reassembly, flow control
  No per-flow state in gateways between networks
    Simple, avoids adaptation and recovery from failure
  Addressing
    8-bit network number, 24 bit host number
    Fails to forsee development of the LAN
    Later split into Class A (national), B (regional), and C (LAN)
1974 Kahn, Cerf develop TCP (with IP included) (December)
  IP later separated for unreliable applications, UDP added
1981 RFCs for TCP and IP
  Initial applications: file transfer, e-mail, voice/video, login

## Slide 90: Internet timeline
1978-1983: NCP replaced by TCP/IP
  Implementations of TCP/IP on many platforms (Clark)
  Mandate from to switch all users on ARPANET from NCP to TCP/IP (1980)
    Not well received
    One-day shutoff of NCP in mid-1982 makes people angry, but not sufficiently convincing
    January 1983: NCP banned from ARPANET “Flag Day” -> The Internet is born
    Some older computers allowed to operate with old NCP for a short time
    Full transition takes several months, finishes at end of 1983
    “I survived the TCP/IP transition” buttons (Y2K bug?)
  Will there be an “IPv6 day?”

## Slide 91: Internet timeline
1982-1985 Application protocols
  SMTP (1982)
  Mockapetris develops DNS (1983)
  telnet (1983)
  ftp (1985)
1980s Jealous non-interoperable competitors
  DOE: MFENet (Magnetic Fusion Energy scientists)
  DOE: HEPNet (High Energy Physicists)
  NASA: SPAN (Space physicists)
  NSF: CSNET (CS community)
  NSF: NSFNet (Academic community) 1985
  AT&T: USENET with Unix, UUCP protocols
  Academic networks: BITNET (Mainframe connectivity)
  Xerox: XNS (Xerox Network System)
  IBM: SNA (System Network Architecture)
  Digital: DECNet
  UK: JANET (Academic community in UK) 1984

## Slide 92: Internet timeline
1986-1995 NSFNet (Jennings/Wolff with funding assist from Al Gore)
  Network for academic/research community
  Selects TCP/IP as mandatory for NSFNet
  Builds out wide area networking infrastructure
  Develops strategy for developing and handing it over eventually to commercial interests
    Prohibit commercial use of NSFNet to encourage commercial backbones
    Leads to PSINet, UUNET, ANS, CO+RE backbone development
1989 WWW
  Tim Berners-Lee develops initial web browser supporting URLs, HTTP, HTML

## Slide 93: Internet timeline
Early 1990s Privatization
  ARPANET decommissioned (1990)
  NSFNet decommissioned (1995) ($200 million spent from 1986-1995)
Early 1990s Architectural issues
  Address depletion
    Multi-class addressing to break 8/24 network/host split in address bits
  Routing table explosion
    Hierarchy and CIDR
  Congestion
    TCP congestion control
1994 Andreessen
  Mosaic web browser

## Slide 94: Packet switching
Kleinrock, MIT (July 1961)
  Theoretical feasibility of communications using packets instead of circuits
  L. Kleinrock, "Information Flow in Large Communication Nets", RLE Quarterly Progress Report, July 1961.
  L. Kleinrock, Communication Nets: Stochastic Message Flow and Delay, Mcgraw-Hill (New York), 1964.

## Slide 95: Conceptual “Internet”
J.C.R. Licklider, W. Clark, MIT (August 1962)
  “On-line Man Computer Communication”
  “Galactic network” concept of globally interconnected set of computers
  Licklider goes to DARPA as head of computer research program (Oct. 1962)

## Slide 96: ARPANET
Roberts, (1966)
  Puts idea of galactic computer network and packet switching together
  Goes to DARPA as program manager
    Plans for building “ARPANET” based on system
    L. Roberts, "Multiple Computer Networks and Intercomputer Communication", ACM Gatlinburg Conf., October 1967.

## Slide 97: ARPANET
Structure and specification (August 1968)
  RFQ to build IMPs (Interface Message Processors)
    Packet switches which route packets
    BBN (Bolt, Beranek, and Newman) wins contract
  Kahn at BBN updates ARPANET design
    Run over any fabric (separation of hardware and network addresses)
    Support for multiple independent networks
First node UCLA (Sept. 1969)
  4 node ARPANET (Dec. 1969) SRI, UCSB, Utah
  Initial hostname/address database (flat file: hosts.txt)

## Slide 98: RFCs
1969: Crocker establishes RFC series of notes
  Official protocol documentation
    Printed on paper and snail mailed at first
    Then available via ftp and now http
    Open and free access to RFCs mandated
    Effective, positive feedback loop
    Key to quick development process (“time-to-market”)
    Has changed considerably as of late...
Jon Postel RFC editor and protocol number assignment

## Slide 99: NCP
Crocker
  Connectivity implemented
  Require a host-to-host protocol standard for two ends to talk to each other
  NCP (Network Control Protocol) defined (Dec. 1970)
  Precursor to TCP
  Deployed from 1971-1972
  Allows applications to be developed on top of network

## Slide 100: E-mail
BBN’s Tomlinson (Mar. 1972)
  Time-shared systems at the time allow users to leave messages for each other
  Extended to remote systems
  Writes first e-mail application to send and read
  Infamous “@” used

## Slide 101: Internetting
ARPANET not the only network in town...
  International Network Working Group (Sept. 1973)
  Goal: run protocols over packet satellite net, packet radio net, and wired ARPANET
  Problems
    NCP can only address networks connected to IMPs on ARPANET
    NCP relied on ARPANET for end2end reliability
    NCP assumed no packet loss: applications halt upon loss
    NCP had no end-end host error control
  Kahn redesigns protocols for internetworking

## Slide 102: Internetting
Kahn’s Architecture
  Each network stands alone
    No changes required to connect to Internet
    Communication between networks handled by gateways
  Communication on a “best-effort” basis
    Least-common denominator
    Source in charge of retransmission
    Host-to-Host flow control (sliding windows and acks)
  Black boxes interconnecting networks (gateways and routers) have no per-flow information
    Simple, avoids complicated adaptation and recovery from failure
  No global control at the operations level

## Slide 103: Internetting
Other issues
  Host-to-Host data pipelining (multiple packets en route)
  Gateway interprets IP headers for routing and performs fragmentation to other networks
  end2end checksums, reassembly of fragments, duplicate detection at end-hosts (much of TCP’s virtual circuit model)
  Global addressing via 32-bit address (IP’s limitation)
    8-bit network number, 24 bit host number
    Fails to forsee development of the LAN
      Later split into Class A (national), B (regional), and C (LAN)
  Interfaces to operating systems
    R. Kahn, Communications Principles for Operating Systems. Internal BBN memo, Jan. 1972.

## Slide 104: Internetting
Kahn brings in Cerf (Stanford) to help implement ideas on multiple OS platforms
  V. Cerf, R. Kahn “A protocol for packet network intercommunication” IEEE Transactions on Communications, May 1974
  TCP draft produced (includes IP) Dec. 1974
ARPA sponsors 3 groups to implement on hosts
  Stanford (Cerf), BBN (Tomlinson), UCL (Kirstein)
  All interoperate
IP later separated (not all apps need reliability)
  UDP added

## Slide 105: Internetting
IP
  Internet Protocol (Sept. 1981) Postel
  http://www.rfc-editor.org/rfc/rfc791.txt
TCP
  Transmission Control Protocol (Sept. 1981) Postel
  http://www.rfc-editor.org/rfc/rfc793.txt
Initial applications
  Goal is resource sharing of systems on ARPANET
    File transfer
    Remote login (telnet)
    E-mail
    Packet voice, packet video (late 1970s)

## Slide 106: Application protocols
SMTP
  Simple Mail Tranfer Protocol (Aug. 1982) Postel
    http://www.rfc-editor.org/rfc/rfc821.txt
DNS
  Hostnames server, SRI (Mar. 1982) Harrenstien
    http://www.rfc-editor.org/rfc/rfc811.txt
  Current hierarchical architecture (Aug. 1982) Su, Postel
    http://www.rfc-editor.org/rfc/rfc819.txt
  Domain Name System standard (Nov. 1983) Mockapetris
    http://www.rfc-editor.org/rfc/rfc882.txt
    http://www.rfc-editor.org/rfc/rfc882.txt
Notes: Before DNS, pushing around an /etc/hosts file

## Slide 107: Application protocols
Telnet
  Telnet protocol (May 1983) Postel, Reynolds
    http://www.rfc-editor.org/rfc/rfc854.txt
FTP
  File transfer protocol (Oct. 1985) Postel, Reynolds
    http://www.rfc-editor.org/rfc/rfc959.txt

## Slide 108: NSFNet
Structure
  6 nodes with 56kbs links
    Jointly managed exchange points
    Statistical, non-metered peering agreements
    Cost-sharing of infrastructure
  Seek out commercial, non-academic customers
    Help pay for and expand regional academic facilities
    Economies of scale
    Prohibit commercial use of NSFNet to encourage commercial backbones
    Leads to PSINet, UUNET, ANS, CO+RE backbone development

## Slide 109: TCP/IP software proliferation
Widespread dispersal leads to critical mass
Case study: Berkeley Unix
  Unix TCP/IP available at no cost (DoD)
  Incorporates BBN TCP/IP implementation
  Large-scale dissemination of code base
  Eventual economies of scale

## Slide 110: Privatization
Commercial interconnection
  US Federal Networking Council (1988-1989)
  MCI Mail allowed
ARPANET decommissioned (1990)
NSFNet decommissioned (1995)
  21 nodes with multiple T3 (45Mbs) links
  Regional academic networks forced to buy national connectivity from private long haul networks
  TCP/IP supplants and marginalizes all others to become THE bearer service for the Internet
  Total cost of NSF program?
$200 million from 1986-1995

## Slide 111: Growing pains
Address depletion
  Multi-class addressing to break up 8-bit network/24-bit host
Explosion of networks
  Routing initially flat, each node runs the same distributed routing algorithm
  Moved to hierarchical model to match commercial reality (IGP, EGP)
    Reduces table size, distributes control (a bit)
  Classless addressing (CIDR)
    Reduces table size
Congestion
  Network “brown-outs”, congestion collapse
  Add congestion control to TCP protocol, not IP

## Slide 112: WWW
CERN (European Organization for Nuclear Research)
  Berners-Lee, Caillau work on WWW (1989)
  First WWW client (browser-editor running under NeXTStep)
  Defines URLs, HTTP, and HTML
  Berners-Lee goes to MIT and LCS to start W3C
    Responsible for evolving protocols and standards for the web
  http://www.w3.org/People

## Slide 113: WWW
NCSA (National Center for Supercomputing Applications)
  Federally funded research center at University of Illinois at Urbana-Champaign
  Andreessen: Mosaic and eventually Netscape (1994)
  http://www.dnai.com/~thomst/marca.html

## Slide 115: Today’s Internet

## Slide 116: Residential access
Driven by networks already in place to the home
  Most common
    Cable TV lines
    Phone lines
  Less common
    Satellite television
    Power lines
Notes: SATV = 1974, CATV = 1948, Phone = 1890

## Slide 117: Residential access: cable
Originally one-way distribution
home
cable headend
cable distribution
network (simplified)

## Slide 118: Residential access: cable
home
cable headend
cable distribution
network (simplified)

## Slide 119: Residential access: cable
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM:

## Slide 120: Residential access: cable
Download faster than upload
  Noise issues with one source vs. many
home
cable headend
cable distribution
network

## Slide 121: Residential access: DSL

## Slide 122: Residential access: DSL
Uses high-frequency spectrum
  Data superimposed onto voice using high-frequencies on existing telephone line
  Voice transmitted in low-frequency spectrum
  Transmissions may disrupt each other
    Low-pass filters typically added to protect legacy devices and DSL modems from each other

## Slide 123: Residential access: DSL

## Slide 124: Internet structure: network of networks
Influenced by decommissioning of NSFNet
  Academic network connecting NSF’s supercomputing sites
  NSF wanted out of the ISP business
  Provided peering points for multiple competing commercial ISPs

## Slide 125: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
  Peers with every other network to reach Internet
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 126: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 127: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Peers with some networks, but still purchases IP transit from tier-1 ISP to reach some portion of the Internet
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 128: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
  solely purchases transit from other networks to reach Internet
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 129: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 130: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
history
You now have:
context, overview, “feel” of networking
more depth, detail to follow!